## Slide 1
自主創新
Innovation Ownership
綠能環保
Sustainable Energy
雲端服務
Cloud Service
無線寬頻
Mobile Broadband
新興市場
Emerging Market
Barcelona Board's I/O
LED/FAN/Button/USB/RTC
Nov 19th 2015
Liao Eden

## Slide 2
Board's I/O control Drivers
0001 Board IO deivers.patch
Drivers
  \kernel\drivers\gpio\iec_board.c //ProcFS For BOARD_io and BOARD_event
  \kernel\drivers\gpio\pm51_gpio.c //ProcFS For FAN_io and 8051 virtual uart
Fix for board’s i/o control drivers build in
  \kernel\drivers\gpio\Makefile
  obj-y += pm51_gpio.o
  obj-y += iec_board.o
Check ProcFS after board io driver ready
  /proc/BOARD_io
  /proc/BOARD_event
  /proc/FAN_io

## Slide 3: Board's I/O status (LED)
PM_GPIO_13 SATA0_LED_ACT
PM_GPIO_14 SATA1_LED_ACT
PM_GPIO_15 SATA0_LED_ERROR
PM_GPIO_16 SATA1_LED_ERROR
PM_PWM_0_GPIO_18 POWER_LEDR
PM_JTAG_TDI_GPIO_20 POWER_LEDW
PM_JTAG_TCK_GPIO_22 WLAN_ACTIVE_LED
PM_JTAG_TCK_GPIO_23 WLAN_ERROR_LED
PM_GPIO_10 USB_ACT

## Slide 4
LED control Format
Format
  # Usage: echo "<item> [<index>] <value>" > /proc/BOARD_io
  # value 0:Off; 1:On; 2:BlinkSlow 3:BlankFast 4:Fail 5:FailBlankSlow
  6:FailBlankFast 7:BlankRandom 8:BlankMix 9:ShortShow
  # "PWR_LED 0|1|2|3|4|5|8|9" * LED System Status
  # "A_LED 1-N 0|1|2|3|7" * LED SATA 1-N ACTIVE led
  # "S_LED 1-N 0|1|2|3" * LED SATA 1-N ERROR led
  # "W_LED 0|1|2|3" * WIFI ACTIVE led
  # "WF_LED 0|1|2|3" * WIFI ERROR led
  # "U_LED 0|1|2|3" * USB BUSY led

## Slide 5
LED control Example
Example
  echo PWR_LED 1 > /proc/BOARD_io //Power While LED ON(Red LED OFF)
  echo PWR_LED 4 > /proc/BOARD_io //Power Red LED ON (While LED OFF)
  echo A_LED 1 1 > /proc/BOARD_io //HDD1 While LED ON
  echo A_LED 2 1 > /proc/BOARD_io //HDD2 While LED ON
  echo S_LED 1 1 > /proc/BOARD_io //HDD1 Red LED ON
  echo S_LED 2 1 > /proc/BOARD_io //HDD2 Red LED ON
  echo W_LED 1 > /proc/BOARD_io //WIFI While LED ON
  echo WF_LED 1 > /proc/BOARD_io //WIFI Red LED ON
  echo U_LED 1 > /proc/BOARD_io //USB Copy While LED ON
  echo PWR_LED 0 > /proc/BOARD_io //Power LED OFF

## Slide 6
HDD LED extend control
0002 HDD LED extend control.patch
Drivers
  \kernel\drivers\scsi\sd.c //For HDD insert or remove
  \kernel\drivers\ata\libata-core.c //For HDD access
ADD patch to kernel source
  //Example
  #define LED_ENABLE 0x4
  #define LED_DISABLE 0x5
  #define LED_OFF 0x0
  #define LED_ON 0x1
  extern void iec_disk_access(int index, int act);
  …

## Slide 7: Board's I/O status (Button)
INPUT
PM_GPIO_17 PWR_BUTTON
USB0_OC_N_GPIO_96 UCOPY_BUTTON
USB1_OC_N_GPIO_97 RESET_BUTTON

## Slide 8
Button control Format/Example
Format
  # Check Button Status
  # Usage: cat /proc/BOARD_event
Example
  cat /proc/BOARD_event
  PWR ON //PWR_BUTTON is pushed for now
  Copy ON //UCOPY_BUTTON is pushed for now
  RST2DF ON //RESET_BUTTON is pushed for now
  NOBTN ON //All BUTTON is released

## Slide 9
Button extend control
0004 Button extend control.patch
Deamon
  btn_dispatcher_iec //For checkout Button status routine
Usage
  Put btn_dispatcher_iec to /etc/init.d/
  chmod a+x /etc/init.d/btn_dispatcher_iec
  Add “/etc/init.d/btn_dispatcher_iec > /dev/null ” to boot sequence xxx.rc
  Fix btn_dispatcher_iec to add action for UCOPY/RESET button pushed
Example
  Power Button push > 4 sec to execute power down
  echo "PWR_LED 3" > /proc/BOARD_io //Set PWR_LED BlinkSlow
  sh -c "poweroff > /dev/null 2>&1"

## Slide 10: Board's I/O status (PM51 GPIO Output)
OUTPUT
PM_PS_ON_3_GPO_5 ZIBGEE_RESET
PM_JTAG_TMS_GPIO_21 WLAN_DISABLE

## Slide 11
PM51 GPIO Output control Format/Example
Format
  # Set PM8051 GPIO 5/21 Value
  # Usage: echo "<item> <value>" > /proc/BOARD_io
  # item : ZB_RST or W_DIS value 0:low; 1:high
Example
  echo “ZB_RST 1” > /proc/BOARD_io //Set PM_GPO_5 to high
  echo “W_DIS 1” > /proc/BOARD_io //Set PM_GPIO_21 to high

## Slide 12: Board's I/O status (FAN)
PM_GPIO_8 FAN_TACH
PM_PWM_1_GPIO_19 PWM0_FAN

## Slide 13
FAN control Format/Example
Format
  # FAN control duty 0-100
  # Usage: echo "<PWM duty>" > /proc/FAN_io
Example
  echo 50 > /proc/FAN_io //Set PM_PW M_1_GPIO_19 duty 50%
Format
  # Check FAN speed
  # Usage: cat /proc/FAN_io
Example
  cat /proc/FAN_io
  2250 //Return FAN speed is 2250 rpm for now

## Slide 14
FAN extend control
0005 FAN extend control.patch
Deamon
  check_fan_lan_sit_iec.sh //For FAN speed control routine
Usage
  Put check_fan_lan_sit_iec.sh to /etc/init.d/
  chmod a+x /etc/init.d/btn_dispatcher_iec
  Add “/etc/init.d /check_fan_lan.sh > /dev/null ” to boot sequence xxx.rc
  Add “echo > /tmp/boot_ok1” after boot finish for start FAN control
check for execute
  cat /tmp/fan_temp
  C0:cpu1temp C1:cpu2temp H0: HDD1temp H1:HDD2temp F:fan_bt_state S:fanspeed //Status
Need Intel “thermal” driver and tool for CPU temperature
Need linux “smartctl” tool for HDD temperature

## Slide 15
HDD Spin up delay Feature
0003 HDD spin up delay.patch
Drivers
  \kernel\drivers\ata\libata.c
phyADD patch to kernel source for power safety. (For Seagate HDD)
  //Example
  #define IEC_HDD_SPIN_UP_DELAY
  #ifdef IEC_HDD_SPIN_UP_DELAY
  volatile long unsigned int hdd_spin_up_lock_flag=-1;
  struct timer_list hdd_spin_up_timer;
  #define HDD_SPIN_UP_LOCK(addr) \
  { \
  while (test_and_set_bit(0, addr) != 0) { \
  ata_msleep(ap, 1); \
  } \
  }
  …

## Slide 16
USB 3.0 driver Patch
0006 USB 30 driver.patch
Drivers
  \kernel\drivers\pci\ && \kernel\drivers\usb\ && \kernel\include\
ADD patch to kernel source for upd720202 USB phy
  //Example
  //Wilson modified for renesas uc720202 USB3.0 S3 suspend issue
  //[b]
  //[m]
  if((pci_dev->vendor == 0x1912)&&(pci_dev->device == 0x0015))
  {
  printk(KERN_INFO "uc720202:pci_pm_suspend\n");
  if (!pci_dev->state_saved)
  {
  …

## Slide 17
RTC Usage
After boot finish, use the hwclock command, read RTC to system
  hwclock --hctosys --localtime
To show system time, use the date command:
  date
  Tue Dec 1 18:10:14 CST 2015
To set system time, use the date command:
  date -s "2016-01-01 00:00:00"
Use the hwclock command after set system time to synchronize an RTC
  hwclock --localtime –systohc
Use the rtcwake command to set wakeup time from RTC
  rtcwake -d rtc0 -m mem -s 120 # Execute RTC wakeup after 120 sec

## Slide 18
Platform Parameters for serial number
shell> mfh list spi_nor
  plat_params start_addr=0x0018E830 size=0x10000
Platform Parameters Table
  serial number offset=0xFFB0 size=0xB //sn_buf[0] != '0' && sn_buf[0] != 0
Use the dd command for read serial number
//serial number start address = 0x0018E830+0xFFB0 = 1697760
  dd if=/dev/mtdblock0 bs=1 count=11 skip=1697760 of=/tmp/serial_num.txt
  cat /tmp/serial_num.txt

## Slide 19: Thank YOU!
Questions and Answers
Notes: 19